## Slide 1: Onsite Sewage and Water
Duke Price
March, 2015
Click on the microphone where shown in each slide to listen to the narrative

## Slide 2: Question 2
How often, if ever, should a septic tank be pumped?
5-7 years

## Slide 3: Question 3
The first groundwater protection rule established in America in:
1610 – “There shall be no man or woman dare to wash any unclean linen, …nor rinse or make clean any kettle, pot or pan,…within twenty feet of the well.” (AGWT, 2003)

## Slide 4: Big Picture
States must comply with federal environmental protection laws
Pollutant levels are set for drinking water (public)
  Boil water notices
Wastewater treatment standards are also set (Clean Water Act)
  Primary, secondary, tertiary treatment

## Slide 5
Virginia has five physiographic provinces
  West to East
    Cumberland Plateau
    Valley and Ridge
    Blue Ridge
    Piedmont
    Coastal plain

## Slide 7: Onsite = Out-of-site (not out-of-mind)
All sewage systems require maintenance
Our private well water is recycled
Recent advances in onsite sewage systems.

## Slide 8: Maintenance
No different than other elements of home
  HVAC, exterior, roof
  Primary: septic tank
  Secondary: bio-filter, attached growth,
  Soil based absorption systems

## Slide 9
What’s in Wastewater?
1. Water (99 Percent)
2. Organics & Nutrients
3. Fats, Oils, and Grease (FOG)
4. Inorganics and other solids
(Hair, cloth)
5. Virus and Bacteria
6. Heavy Metals
7. Ammonium, Phosphates
Notes: ‹#›
10
Because as you might have expected, wastewater has some things in it that can cause disease and sickness. And it effects the receiving environment--the absorption area. We measure these constituents by determining BOD, FOG, and TSS.
BOD5 stands for “ biochemical oxygen demand”. The BOD test models aerobic waste treatment. It measures oxygen taken up during the oxidation of organic matter. It provides us insight on how strong the wastewater is and how much of the ecosystem’s resources must be devoted to getting rid of the organics. Organics means having carbon compounds. BOD testing has its widest application in measuring waste strength and in evaluating the efficiency of treatment processes.
TSS stands for “Total Suspended Solids” and relates to the solids from organics or inorganics that “cloud” the wastewater. It measures the tiny particles that don’t settle out.
FOG is derived from body oils, soaps, and cooking. The organic components in general come from toilet waste and garbage disposals.
Heavy metals can come from clothing (mechanic) and various cleaners.

## Slide 10
Why do we regulate? (The Hydrologic Cycle)

## Slide 11: Community
Sewage – cluster systems
  One owner
  Loudoun, Franklin Counties
Water – public water supplies
  Testing, maintenance
  Office of Water Programs

## Slide 14: System Failure
Notes: ‹#›
15

## Slide 17
Notes: ‹#›
19
Talk about concept of creeping failure with a sewage system disposing of septic tank effluent.
Talk about pretreated systems that do the work for the soil.

## Slide 18: What is a well?
A deep hole or shaft sunk into the earth to obtain water, oil, gas, or brine (dictionary.com)
i.e., man’s attempt to get water from stone

## Slide 19
Ground Water Use in the United States (1995)
Notes: ‹#›
21
Ground water is an important source of drinking water for every State. (U.S. Geological Survey, 1998.)

## Slide 20: DOH website
http://www.vdh.virginia.gov/